## Slide 1
Safety Moment
Choke Manifold Pressure Test
Disclaimer: this safety moment is designed to prevent similar incidents occurring. All guidance herein is provided in good faith and Step Change in Safety nor its member companies accept responsibility for any inaccuracies or omissions contained within this safety moment.

## Slide 2
Pressure testing of a choke manifold was being undertaken in an onshore well test pressure test bay.
After the test pressure was applied, the workshop foreman and technician entered the test area to visually check the manifold for leaks.
What could go wrong? What could be the consequences?
Choke manifold pressure test
DISCUSS

## Slide 3
What happened:
A thermowell failed under pressure and was ejected at approx. 100 mph, striking the technician on the knee with a force equivalent to being hit by a family car.
Severe corrosion had affected the integrity of the thread connection. Pressures encountered during testing overcame the mechanical strength of the thread and caused the thermowell to be ejected.
Choke manifold pressure test
Notes: A thermowell is a pocket that penetrates into a pipe or vessel to allow measuring of temperature inside the pipe/vessel.

## Slide 4
What behaviours and steps would prevent this from happening?
DISCUSS
What similar situations might you face?
What might you do differently today in your work?
Choke manifold pressure test

## Slide 5
Steps which could have been taken to avoid this incident:
Pressure retaining threads should be inspected for corrosion and wear with calibrated thread gauges during routine maintenance and before testing.
A review of the risk assessment had not been conducted before performing the pressure test.
The pressure testing bay was built to contain the failure of equipment but was not fitted with viewing ports, which meant the technicians needed to enter the bay to check for leaks.
Choke manifold pressure test

## Slide 6: Which of the 7Cs are involved in this safety alert?
Change management
Communication
Complacency
Control of work
Competence
Culture
Commitment
Did this presentation result in discussion that could lead to creating another alert to share with industry? Please contact : info@stepchangeinsafety.net
Choke manifold pressure test