## Slide 1
Disclaimer: this safety moment is designed to prevent similar incidents occurring. All guidance herein is provided in good faith and Step Change in Safety nor its member companies accept responsibility for any inaccuracies or omissions contained within this safety moment.
The risks of multi-tasking
Notes: This safety moment is adapted from a case study published in ‘Human Factor - First Steps’

## Slide 2: Human factors in design
What was happening?
Routine drilling operations
A stand of drill pipe was clamped in the slips, raised and manually held on the brake
A roughneck stepped into the hazardous area of the rig floor
Notes: There was a stand of drill pipe clamped in the slips, raised and manually held on the brake.
A roughneck stepped into the hazardous area of the rig floor.
The driller reached for the microphone to alert the roughneck.
What could go wrong?

## Slide 3: Human factors in design
Stepping on the manual brake
Holding the hydraulic brake
Pushing the microphone button with knee
Speaking on microphone
The driller was…
What could go wrong?
Notes: The driller was simultaneously holding the drill pipe in position whilst using the microphone to alert the roughneck on the drill floor

## Slide 4: Human factors in design
What Happened?
As he reached for the microphone, he slightly released pressure on the brake
The top drive descended, bending the drill pipe, which fortunately did not spring out
A 27kg pipe-guide fell 90 feet to the floor, narrowly missing the roughneck
Pressure released from brake and top drive descended
Leaned Left
Notes: As he reached for the microphone, he slightly released pressure on the brake
The top drive descended, bending the drill pipe which fortunately did not spring out
A 27kg pipe-guide fell 90 feet to the floor, narrowly avoiding the roughneck
If the brake-control had been entirely released, the brake would have applied automatically. Unfortunately, a small release in hand-pressure was enough to remove the brake.
Keeping your arm steady during a task requires concentration and balance. Changing your position affects this fine-control. The movement towards the microphone reduced pressure on the brake and the top drive descended.

## Slide 5: Human factors in design
Equipment design: The system was known to be difficult to operate
Management of small changes: Over time, more equipment had been added and controls were placed wherever they could fit without considering how they would be operated
Recognising risk and raising concerns: People accepted the poor layout and controls, and got on with the job
What led to this happening?
Everyone has the ability to manage at least one of these barriers
Notes: Accepted the poor layout and controls, and got on with the job

## Slide 6: Human factors in design
What can we learn from this?
Any change can have consequences. Consider if changes in your workplace have impacted safe working
Speak up if equipment or processes are difficult to use. Identify workarounds and don’t accept them
Routine tasks can still be hazardous and people become normalised to risks. Challenge yourself and others
Do you have similar issues at your worksite?

## Slide 7: Human factors in design
Have a look at the Human Factors in Design questions in the online HF tool to find out how well you are performing
https://humanfactors.atlasknowledge.com/assessment/10

## Slide 8: Human factors in design
Which of the 7Cs are involved in this safety alert?
Change management
Communication
Complacency
Control of work
Competence
Culture
Commitment
Did this presentation result in discussion that could lead to creating another alert to share with industry? Please contact : info@stepchangeinsafety.net