## Slide 1
Disclaimer: this safety moment is designed to prevent similar incidents occurring. All guidance herein is provided in good faith and Step Change in Safety nor its member companies accept responsibility for any inaccuracies or omissions contained within this safety moment.

## Slide 2: Hide this slide
This pack contains an overview of the IOGP Process Safety Fundamentals with relevant incident examples.
Whilst not all of the incidents occurred within our industry, the learnings remain applicable.
You may wish to use this pack during safety meetings or break it up and use the individual sheets for your toolbox talks.
Each slide contains
An overview of the Process Safety Fundamental
  An applicable incident learning or industry tool
    Engagement & discussion prompts

## Slide 3: Why do we have Process Safety Fundamentals?
The Process Safety Fundamentals (PSFs) are a set of basic principles for front-line workers, supervisors, and managers that emphasise existing good practices to prevent fatalities from Process Safety Events.
Between 2007 – 2017, 128 lives could potentially have been saved by following these Process Safety Fundamentals.

## Slide 4
What process safety hazards impact your daily operations?
How do you improve process safety hazard awareness and what is your role in controlling them?
How do you identify and discuss process safety hazards before starting a task?
We respect hazards
We improve our understanding of process safety hazards at our location and our roles in controlling them.
We are vigilant about the potential impacts of uncontrolled process safety hazards.
We discuss process safety hazards before starting a task.
We bring forward process safety hazards to be included in activity risk assessments.
Dynamic Risk Assessment
Incident investigations identify lack of hazard awareness as an underlying cause of many process safety events.
It is important that we understand the process safety hazards here and be aware of the harm they could cause if we lost control of them.
There are several tools we can use to identify and communicate hazards.
Templates shown are from the Safe Working Essentials Toolkit – a suite of tools covering the control of work elements.

## Slide 5
Well blowout - What happened?
Wells were drilled, the topside facilities were installed. Next, the wells were to be tied back to the platform.
The pressure-containing cap was removed. There was no significant pressure recorded under the cap prior to removal, but the blowout occurred within hours.
Oil and gas flowed for over ten weeks before a relief well was successfully put in place.
In addition to this, there was an ignition of the release, resulting in a fire which continued for two days before the flowing fluids were brought under control and the fire extinguished.
What Went Wrong - Breach of Procedures
The Well Construction Standard required two proven independent barriers to be in place.
  The integrity of the primary cemented 95/8 casing shoe track was never proven.
  Only one of the secondary barriers (pressure containing caps) was installed and this was later removed and not re-instated.
In addition to this, monitoring of the fluid in the well bore to maintain a safety margin in the bottom hole pressure did not take place [1].
[1] Another form of well control barrier is to ensure that the hydrostatic head of fluid in the well bore always exceeds the reservoir pressure, this will prevent fluid from flowing to surface.
We apply procedures
We use operating and maintenance procedures, even if we are familiar with the task.
We discuss the key steps within a critical procedure before starting it.
We pause before key steps and check readiness to progress.
We stop, inform supervision and avoid workarounds if procedures are missing, unclear, unsafe, or cannot be followed.
We take time to become familiar with, and practice, emergency procedures.
How are the applicable procedures communicated prior to starting a task?
What action do you take if procedures are missing, unclear, unsafe or cannot be followed?
How do you familiarise yourself with the procedures that apply in an emergency?

## Slide 6
What happened?
Platform inspections had several findings around the planning & inspection of scaffold structures:
There were several breaches of the 50mm allowance rule to avoid damage to in-service plant and equipment through movement of the scaffold structure or plant.
Escape routes were also found to be compromised due to scaffold blocking the routes.
The team had not identified the need to properly communicate or seek approval for when escape routes were compromised by scaffolding.
Initial & ongoing Scaffold inspections did not identify these issues.
Consider sustaining barriers when siting scaffolding:
Blockage of, or restriction to primary walkways & escape routes.
Blockage of gas detection, flame detection, smoke detection, fusible loops or frangible bulbs.
Blockage of deluge nozzles or sprinkler heads.
Blockage of PA Speakers, emergency lighting or navigation aids e.g. lights, foghorns.
Access to critical equipment such as fire hydrants, MAC Points, critical valves, access doors, phones etc.
We sustain barriers
We discuss the purpose of hardware and human barriers at our location.
We elevate how our tasks could impact process safety barriers.
We speak up when barriers don’t feel adequate.
We perform our roles in maintaining barrier health and alert supervision to our concerns.
We use an approval process for operations with degraded barriers.
What are the barriers in place at your site to prevent process safety hazards?
What would you do if you suspected that a barrier may be inadequate?
Which barriers are your responsibility to maintain, and how do you do that?

## Slide 7
Air Gas Facility – Fatal Explosion
A nitrous oxide transport lorry exploded whilst being filled at a chemical manufacturing site in Florida.
The explosion killed 1 person and caused significant damage to the site.
Nitrous oxide is stable and can be safely handled; however, under certain conditions it can decompose explosively.
A pump used to transfer nitrous oxide into a trailer heated the gas above its safe operating limit and triggered a violent decomposition reaction.
How can you verify that you remain within operating limits?
What actions do you need to take if operating limits are exceeded?
If normal operating limits require to be exceeded, how is approval sought and verified?
We stay within operating limits
We discuss and use the approved limits for our location.
We escalate where we cannot work within operating limits.
We alert supervision if an alarm response action is unclear or the time to respond is inadequate.
We obtain formal approval before changing operating limits.
We confirm that potential for overpressure from temporary pressure sources has been addressed.
Key findings:
No review of the system was carried out to identify and control process safety hazards
Installed safeguards failed to prevent the explosion
Click  YouTube logo to play video full screen in browser
Notes: https://youtu.be/blzC6D0p9lM

## Slide 8
We maintain safe isolation
We use isolation plans for the specific task, based on up-to-date information.
We raise isolation concerns before the task starts and challenge when isolation plans cannot be executed.
We check for residual pressure or process material before breaking containment.
We monitor the integrity of isolations regularly and stop to reassess when change could affect an isolation integrity.
We confirm leak-tightness before, during , and after reinstating equipment
Release of high - pressure steam from flange during maintenance resulting in life changing injury
During work to a steam turbine, a pipe fitter and apprentice were dismantling a flange on a 6” high pressure steam line.
The line had been isolated but the isolation procedure and safeguards failed, causing the line to become pressurised with high pressure steam.
This caused the flange to spring open and eject condensate and steam over two men, causing life changing injuries to both men.
Does your isolation have passing valves? How would you know?
What precautions do you take on the first breaking of containment?
How do you ensure that the system has no pressure before breaking containment?
How do you verify that an isolation is still suitable following a delay to the task?
How was the fundamental breached / applicable?
The main steam isolation valve had been passing. During previous work on the equipment, this had been controlled by a constant bleed to prevent an increase in pressure.
During a delay to the workscope (waiting for parts) the bleed had been closed, resulting in the pipework pressurising up to mains steam pressure (80 Bar) over a period of time.
On restarting the work, the isolation certificate and isolation point still existed but the isolation was not proved by opening the bleed valve.

## Slide 9
We walk the line
We use up-to-date documentation (e.g. Piping and Instrumentation Diagrams) that accurately reflect installed systems and equipment).
We physically confirm the system is ready for the intended activity (e.g. valve positions, line up of relief devices, etc.).
We alert supervision to identified documentation and readiness issues before operation.
Missing ½ inch plug identified during line walk, preventing potential significant hydrocarbon release
During a planned full platform shutdown, a production test separator was removed from service for maintenance.
The system was isolated, depressurized and a section of pipework replaced.
A successful leak detection took place.
The system was deisolated but the plant was not ready for restart so the system remained offline.
Several days later, as the plant was being readied to go back online, a member of the work party raised concerns that the process for reinstatement may not have been correctly followed as no records were in the hand over to state a full system line walk had taken place.
When queried, the work party advised that only a partial line walk had taken place.
Activity to bring the plant online was stopped and a full system line walk carried out as per company procedures.
During the line walk, it was discovered the level transmitter isolation valves were still closed and a ½ inch plug was missing from the tapped flange used as the leak test injection point.
If the line walk had not been completed, the tapped flange would have remained open ended, creating a potential significant hydrocarbon leak. It would have also resulted in no level being observed on the level transmitter during start-up.
How do you ensure proper line walks take place prior to reinstatement of plant?
What procedures are in place at your site for the safe reinstatement of plant?
How do you manage a change that occurs during plant reinstatement?
This moment was based on the Joined-up Thinking Pack Hydrocarbon Release Prevention – Plant Reinstatement

## Slide 10
We control ignition sources
We identify, eliminate, or control the full range of potential ignition sources during task risk assessment and during job preparation and execution.
We minimize and challenge ignition sources even in “non-hazardous” areas.
We eliminate ignition sources during breaking containment and start-up and shutdown operations.
What potential sources of ignition are there at your site?
How are these controlled?
How do you minimize ignition sources in different areas of site?
How do you eliminate ignition sources during breaking containment?
Scaffold board fire ignites skip contents:
A single flame detector activated in the control room in the middle of the night and an operator was sent to check the location.
The operator arrived at the location to find smoke coming from the general waste skip.
Boards on a scaffold structure were ignited by the adjacent generator exhaust. The hot embers from the scaffold boards ignited the fire in the skip below.
The GPA was activated, production was shut down and the generator was taken offline.
The fire team responded and extinguished the fire.
Key Finding:
The potential for the scaffold boards to ignite due to the close proximity to the hot surface of the exhaust generator had not been identified.

## Slide 11
We recognise change
We look for and speak up about change.
We discuss change and involve others to identify the need for management of change (MOC).
We review the MOC process for guidance on what triggers an MOC.
We discuss and seek advice on change that occurs gradually over time.
Unplanned plant modification resulting in hydrocarbon release
A ~560kg high pressure gas release occurred when a small-bore tubing fitting assembly ruptured as a result of vibration fatigue after 11 days in service.
What went wrong?
A change to the SBT was made to simplify the sample collection process for the technician.
There was no Management of Change carried out or appreciation of the effect of vibration upon unsupported SBT assemblies.
The work was undertaken with the best intent but circumvented all the approval controls.
Ask yourself: Could that happened here?
How is change managed and communicated at your site?
How do you remain vigilant to changes and speak up about them when identified?
What is your sites process for management of change?

## Slide 12
Courrieres mine disaster
One of Europe’s worst mining disasters took place in northern France on the 10th of March 1906 when an underground explosion and fire killed 1,099 and injured hundreds more.
The unexpected:
A few days prior to the explosion, smoke and toxic gas were detected, however, work in the mine continued.
The day before the main explosion, a fire was reported deep in the mine. Workers attempted to seal off the area to contain and suffocate the flames, but flammable gas leaked from the walls near the fire.
It is thought that the flammable gas ignited, spurring a huge explosion that sent flames racing through the rest of the mine.
We stop if the unexpected occurs
We discuss the work plan and what signals would tell us it is proceeding as expected.
We pause and ask questions when signals and conditions are not as expected.
We stop and alert supervision if the activity is not proceeding as expected.
What type of signals would cause you to stop the job?
If signals indicate that a job should be paused / stopped what would allow it to restart?
What additional actions should be taken if a job required to be stopped?
Notes: Expect responses to be similar to - Stop the Job, reassess, ER? Weak Signals, MAKE AREA SAFE

## Slide 13
Hydrocarbon release at 3rd stage Natural Gas Liquids (NGL) knock out pot detected and reported by an operator during daily routine
An operator carrying out routine checks detected a slight smell of gas which he was unable to locate visually or with the use of a personal gas monitor.
The smell was reported to his supervisor who agreed to the use of a thermal imaging camera to detect the source.
A permit was raised and the camera was used to check all the pipework and valves in the area.
A wisp of gas was identified coming from a section of the pipe with slight scabbing on it. Using the gas meter there was no reading at 50cm, 10cm or 5cm. Only when placing the hose from the portable gas meter directly at the scab was a reading of 3.5%Vol detected.
The supervisor was informed and a risk assessment was conducted to determine that it was safe to continue operating in the area with suitable control measures in place.
As a result of the observation, the decision was taken by the asset team to shut down part of the plant in order to effect a permanent repair.
Historically weeps like this would have gone undetected until they were significantly worse, creating the potential for a Major Accident event. Depending on circumstances, it could result in a reportable gas release or a fire/explosion if an ignition source were present.
We watch for weak signals
We proactively look for indicators or signals that suggest future problems.
We speak up about potential issues even if we are not sure they are important.
We persistently explore the causes of changing indicators or unusual situations.
What sort of weak signal might indicate future problems?
If you identify a potential issue, what further actions do you take?
How do you continue to be proactive in looking for weak signals?

## Slide 14
Disclaimer: this safety moment is designed to prevent similar incidents occurring. All guidance herein is provided in good faith and Step Change in Safety nor its member companies accept responsibility for any inaccuracies or omissions contained within this safety moment.