## Slide 1: Safe Mechanical Lifting & the Prevention of Falling Objects
Disclaimer: this safety moment is designed to prevent similar incidents occurring. All guidance herein is provided in good faith and Step Change in Safety nor its member companies accept responsibility for any inaccuracies or omissions contained within this safety moment.
Photo Credit: Jan Berghuis
Notes: Familiarise yourself with the slides and the animation before presenting.
Speaker notes are included.

## Slide 2: Delete this slide
The intention of this pack is to create awareness of the risks associated with lifting operations and falling objects.
Contained within this pack:
1 Safety Moment
8 Mini Safety Moments
You may wish to use this pack during safety meetings or break it up and use the individual sheets for your toolbox talks.
Safe Mechanical Lifting & the Prevention of Falling Objects

## Slide 3: About this Safety Moment
This Safety Moment is based on an incident which occurred in the UK North Sea.
The intention of this presentation is to create awareness of the risks associated with lifting and the importance of adhering to the Life Saving Rules.
Safe Mechanical Lifting & the Prevention of Falling Objects

## Slide 4: The Lift
The deck crew were tasked with lifting the compactor from the 16ft container.
The right hand door was opened to attach the load to the crane and provide line of sight for the banksman.
Banksman
Safe Mechanical Lifting & the Prevention of Falling Objects

## Slide 5: The Lift
The deck crew were tasked with lifting the compactor from the 16ft container.
The right hand door was opened to attach the load to the crane and provide line of sight for the banksman.
Once the crane hook was connected, the load handler retreated to this position.
Banksman
Load Handler
Safe Mechanical Lifting & the Prevention of Falling Objects

## Slide 6: The Lift
The deck crew were tasked with lifting the compactor from the 16ft container.
The right hand door was opened to attach the load to the crane and provide line of sight for the banksman.
Once the crane hook was connected, the load handler retreated to this position.
Banksman
As the lift starts, the Load Handler approaches the container to open the left door…
What are the risks of doing this?
Load Handler
Safe Mechanical Lifting & the Prevention of Falling Objects

## Slide 7: The Incident
As the Load Handler unlatched the door, the load skewed left and forward as it centred beneath the crane hook, striking the left door.
The door struck the Load Handler, throwing them backwards & injuring them.
Location of Load Handler after being struck
Safe Mechanical Lifting & the Prevention of Falling Objects
Banksman

## Slide 8: Life-Saving Rules
Which elements of these Life-Saving Rules could have prevented this incident from occurring?
I position myself to avoid moving objects
I establish and obey barriers and exclusion zones

## Slide 9: Step Change in Safety 7 Cs
How do YOU recognise change has occurred in YOUR job?
Are YOU sure safety critical communication is mutually understood and acted upon?
Is YOUR work adequately controlled from a safety perspective?
Do YOU feel competent to do the job YOU are asked to do?
What is the worst thing that could happen today? What would YOU do?
How are YOU playing YOUR part in making YOUR worksite safer?
Do YOU feel pressure to maintain production or avoid taking equipment offline?
Safe Mechanical Lifting & the Prevention of Falling Objects
Notes: The Step Change in Safety 7 C’s are key indicators of safety.
Which of these played a part in this incident?
Additional question - ask people to reflect on which of these they influence and/or if they think they could be improved here

## Slide 10
Disclaimer: this safety moment is designed to prevent similar incidents occurring. All guidance herein is provided in good faith and Step Change in Safety nor its member companies accept responsibility for any inaccuracies or omissions contained within this safety moment.
Photo Credit: Jan Berghuis
Safe Mechanical Lifting & the Prevention of Falling Objects

## Slide 11: Failure of lifting equipment – 2.6t dropped object
How do you ensure the lift plan and equipment is fit for purpose?
The operation was to transfer a riser pup joint
A 3t soft sling in poor condition was connected directly to the pad eye of the lifting tool (no shackle between soft sling and lifting tool)
The soft sling failed and the load fell 5ft
Failure of lifting equipment – 2.6t dropped object
Position of banksman

## Slide 12: In the line of fire of falling cargo – Forklift Operation
A lorry driver arrived at site with cargo
The driver left the lorry side for the safe zone whilst the forklift driver offloaded the cargo
As the cargo was offloaded, the driver re-entered the operational area
The load fell from the container whilst the driver was in the line of fire
The driver will never work again
Position of banksman
How do you control your safe zones and barriers?
In the line of fire of falling cargo – Forklift Operations

## Slide 13: Fatality – Rope access technician fell to sea
After completing a potential dropped object sweep under deck, a rope access technician was ascending back up
On reaching the access hatch, both the main safety lines sheared on a sharp edge
The rope access technician fell to sea and was killed
The incident could have been prevented if the task was planned correctly with suitable safety measures in place
Position of banksman
How do you protect your ropes against sharp edges?
Fatality – Rope access technician fell to sea

## Slide 14: Lattice beam failed during lifting operation
An alloy scaffold lattice beam failed during a lifting operation
The beam was part of a rigging task to remove a 450kg actuator
The beam failed before the actuator was lifted so no dropped from height resulted
Position of banksman
Corrosion point of failure on top chord
What do you do to verify that there is no significant corrosion on you scaffold lift beams?
Lattice beam failed during lifting operation
Notes: Failure due to corrosion where scaffold clips had previously been fitted
Ineffective pre use checks were completed and lack of control over the inspection regimes for the beams

## Slide 15: Hand placement – Injury during lifting operation
When landing the container it reached the injured persons (IP’s) waist height
The IP extended their right hand to steady the load
Unexpected movement trapped the IP’s hand between an adjacent static container subsequently crushing the IPs hand
Position of banksman
What do you do at your site to prevent these types of injuries occurring?
The IP’s body position at time of injury.
Note that the bottom of the container on the left would have been at waist height at time of incident
Hand placement – Injury during lifting operation

## Slide 16: Dropped scaffolding fitting
The task was to erect a small platform on top of a crane
A bag of fittings were carried to the top and laid next to the handrail
A fitting (832g) fell from the bag, over the kickboard 25m landing on the roof of machinery
Position of banksman
What do you do to prevent dropped objects when storing materials at elevated work sites?
Dropped scaffolding fitting

## Slide 17: Potential dropped object due to unsecured door
Position of banksman
Potential dropped object due to unsecured door
A flat pack spooler was being lifted from a vessel
During the lift, a storage door had opened revealing a small unsecured tool box
On investigation, it was found the anti-luce drop lock had no means of secondary retention during transport
How would the pre-lift checks at your
site have prevented this ?
Notes: Secondary retention – Antiluce drop lock had no means of secondary retention
Pre-lift checks – Should have been checked for PDO’s and secondary retention on lock

## Slide 18: Potential dropped objects
These items were found during one platform clean-up campaign in 2016 and were all potential dropped objects (PDOs)
Position of banksman
When was a sweep for PDOs last carried out at your site?
What can you do to prevent PDOs?
Potential dropped objects