## Slide 1: Confined Space Entry
Disclaimer: this safety moment is designed to prevent similar incidents occurring. All guidance herein is provided in good faith and Step Change in Safety nor its member companies accept responsibility for any inaccuracies or omissions contained within this safety moment.

## Slide 2: About this Safety Moment
This Safety Moment is intended to highlight how the IOGP Life Saving Rules and Step Change in Safety 7 Cs of safety can be applied to keep people safe when working in confined spaces.
It is based on the Accident Investigation Board (AIBN) safety investigation of a fatality on board the chemical tanker Solstraum on the 4th of February 2011.
Click here for the AIBN Investigation Report
This incident involved a certified and experienced worker who was familiar with the worksite.
Confined Space Entry
Notes: As per notes on screen – you may wish to remove this slide and say it during the cover slide

## Slide 3: The task
You are onboard a cargo tanker transporting a hazardous product.
Your task is to take samples of the cargo fluid by lowering a sampling tube into the tank attached to a steel tape
What could go wrong?
Confined Space Entry
Notes: Set the scene for the audience:
You are doing this task – what could go wrong?

## Slide 4: The Snag
The sampling tube (left) snagged on the heating coils (right) at the bottom of the tank.
Attempts were made to retrieve the sampling tube, but they were unsuccessful.
Confined Space Entry
Notes: The Snag – the tub got snagged on the heating coils.
Attempts were made to retrieve it, but they were unsuccessful.

## Slide 5: Safe System of Work
The cargo was offloaded & nitrogen blanket applied… A number of steps had to be taken to clean the tanks and make them safe. These steps included:
Pre & Post wash flushing
Cold & hot water washes
Smell test & gas test
Ventilation
Permit & Escape Plan
Escape Equipment & Standby Man
Mopping & Drying
Confined Space Entry
1hr
10⁰C
2hr
70⁰C
5min
10min
Notes: As per the notes on the screen, click through the control measures.

## Slide 6: Safe System of Work
The cargo was offloaded & nitrogen blanket applied… A number of steps had to be taken to clean the tanks and make them safe. These steps included:
Pre & Post wash flushing
Cold & hot water washes
Smell test & gas test
Ventilation
Permit & Escape Plan
Escape Equipment & Standby Man
Mopping & Drying
Confined Space Entry
1hr
10⁰C
2hr
70⁰C
5min
10min
After the cold wash was complete, the pumpman put the fan on for 5 minutes, asked his colleague to stand watch, then entered the tank…
Notes: As per the red note, short cuts were taken and the pumpman entered the space.
Discuss.

## Slide 7: The confined space
The pumpman, wearing a filter mask, climbed down into the tank and subsequently collapsed.
His colleague raised the alarm, the emergency response team lifted him from the space within 15minutes.
Despite efforts to save his life, he was later declared dead.
The atmosphere within the space was found to be oxygen deficient (>7% O2)
Confined Space Entry
Notes: As per the notes on the screen.
There is further detail in the investigation report which details that the pumpman attempted a breath hold entry to descend the 10m ladder, cross the tank floor, retrieve the snagged sampling tube and return. He made it half way across the tank bottom before turning around and attempting to escape. He collapsed half way back up the ladder and fell to the tank bottom.

## Slide 8: Life Saving Rules
Confined Space Entry
Which parts of these Life Saving Rules could have prevented this?
Notes: The Life Saving Rules are there to keep us safe.
Bypassing Safety Controls: no authorisation before deviating from the cleaning procedures and CSE procedures
Confined Space: the pumpman only had 1 of the required controls in place (standby man)
Work Authorisation: the pumpman did not have work authorisation to enter the tank.

## Slide 9: The Step Change in Safety 7 Cs
Which of the 7C’s played a part in this incident?
Confined Space Entry
How do YOU recognise change has occurred in YOUR job?
Are YOU sure safety critical communication is mutually understood and acted upon?
Is YOUR work adequately controlled from a safety perspective?
Do YOU feel competent to do the job YOU are asked to do?
What is the worst thing that could happen today? What would YOU do?
How are YOU playing YOUR part in making YOUR worksite safer?
Do YOU feel pressure to maintain production or avoid taking equipment offline?
Notes: The Step Change in Safety 7 Cs
Change management – should have been used when deviating from the cleaning procedure
Communication – the change should have been communicated to management, the entry to the space should have been communicated
Complacency – the cleaning task was routine, it is possible the team had become complacent in carrying it out
Control of work – the safe system of work for confined space entry was not followed
Competence – the pumpman was experienced
Culture – it is possible the safety culture on board was lacking
Commitment – the team failed to commit to doing the job correctly

## Slide 10: Play your part
Did this presentation result in discussion that could lead to creating another alert to share with industry? Please contact : info@stepchangeinsafety.net