## Slide 1: Under Pressure
Disclaimer: this safety moment is designed to prevent similar incidents occurring. All guidance herein is provided in good faith and Step Change in Safety nor its member companies accept responsibility for any inaccuracies or omissions contained within this safety moment.
Notes: Familiarise yourself with the slides and the animation before presenting.
Speaker notes are included.

## Slide 2: About this Safety Moment
This Safety Moment is based on an incident which occurred in November 2019 in the Norwegian sector of the North Sea.
2 people were seriously injured when a 3.4l nitrogen cylinder was being filled to 200bar.
The intention of this presentation is to create awareness of the risk associated with over pressurisation.
Under Pressure
Notes: As per notes on slides – you may wish to remove this slide and say it during the cover slide

## Slide 3: The Task
N2 cylinder removed from cabinet
N2 source connected to booster pump input
N2 cylinder connected to booster pump output
3 people were involved in the task - their positions relative to the equipment is shown
N2
Source
N2
Cylinder
Booster Pump
The task was to fill the
N2 Cylinder to 200bar.
What could go wrong?
Under Pressure
Notes: The slide is animated.
a - The nitrogen cylinder which needed filling was removed from the cabinet.
b - A booster pump was used and it was connected to the platform nitrogen system (shown here as a large bottle)
c - The booster pump was connected to the nitrogen cylinder which needed filling
d - the personnel involved in the task were located in the approximate positions relative to the equipment.
Question to the team - The task was to fill the nitrogen cylinder to 200bar. What could go wrong?
Expect to get responses, if the audience need encouragement, you can suggest things such as…
Over pressure
Failure of hose - hose whipping around
Failure of booster pump
Pressure release
Failure of threaded connection
Connecting the equipment the wrong way around
Using the wrong gases

## Slide 4: The Incident
N2
Source
Booster Pump
The N2 cylinder catastrophically failed when it was pressurised beyond the 200bar service pressure
Injuries:
Suffered life threatening injuries
Seriously injured
Unharmed
Under Pressure
Notes: The Nitrogen Cylinder catastrophically failed when it was over pressurised, splitting into 2 deformed projectiles.
1 person suffered life threatening injuries
1 person was seriously injured
1 was unharmed

## Slide 5: What went wrong?
N2
Source
N2
Cylinder
200bar
Booster Pump
1. Pressure gauge known to be faulty
2. Booster pump rated to 700bar
4. No overpressure protection device
6. Booster pump not tagged, no user manual or maintenance programme
3. Unable to set Booster pump at desired pressure
7. Booster pump out of certification
10. Crew had little or no experience with the pump
5. Cylinder not secured
8. 2 of 3 crew did not sign onto permit
Under Pressure
9. Lack of supervision
Notes: 10 key issues were identified during the incident investigation:
1 - Pressure gauge was known to be faulty, but the equipment was not removed from service
2 - Booster pump was rated to 700bar - significantly in excess of the 200bar service pressure of the nitrogen cylinder
3 - Booster pump pressure could not be set to a desired pressure - such as 200bar in this case.
4 - No overpressure protection device, preventing the cylinder being overfilled.
5 - Cylinder was not secured. If it was, it may not have become a projectile
6 - Booster pump was not tagged, had no user manual or instructions and have no maintenance routines assigned to it - as such, the booster pump was out of certification
8 - Permit to work adherence was poor, only 1 person signed onto the permit
9 - Lack of supervision, meaning these issues were not identified
10 - The team involved in the task had little or no experience in using the booster pump.

## Slide 6: Step Change in Safety 7 Cs
Which of the 7C’s played a part in this incident?
How do YOU recognise change has occurred in YOUR job?
Are YOU sure safety critical communication is mutually understood and acted upon?
Is YOUR work adequately controlled from a safety perspective?
Do YOU feel competent to do the job YOU are asked to do?
What is the worst thing that could happen today? What would YOU do?
How are YOU playing YOUR part in making YOUR worksite safer?
Do YOU feel pressure to maintain production or avoid taking equipment offline?
Under Pressure
Notes: The Step Change in Safety 7 C’s are key indicators of safety.
Which of these played a part in this incident?
Additional question - ask people to reflect on which of these they influence and/or if they think they could be improved here

## Slide 7: Discussion
Similar incidents have also occurred before - we need to prevent recurrence.
If you operate similar equipment, what controls are in place to prevent this from occurring here?
What standards do you have in place to prevent over-pressurisation of equipment?
  Engineering barriers?
  Testing & Maintenance?
  Information, Competency & Training?
  Control of work, toolbox talks?
Over pressurisation can occur when pressure & leak testing, filling cylinders & accumulators and when injecting, cleaning and gas freeing systems.
Under Pressure
Notes: Further discussion points you might want to raise with the group:
1 – Can anyone remember a similar incident in the North Sea? Eighteen years ago a mechanical technician lost part of his arm when the pulsation damper he was charging catastrophically failed. The individual thought he was charging a high pressure damper (circa 100barg) when actually, he was charging a low pressure damper (2barg). It has happened in the past…..how do we retain the hard lessons learnt?
2 - Operating similar equipment - do we have the right controls in place to prevent this happening here? (you may wish to flick back to Slide 5, run through them point by point to confirm).
3- We should have barriers in place to prevent incidents like this occurring. What do we have in place here to prevent it occurring?
Engineering - Do we have the correct pressure gauges & over pressurisation devices? Are they correctly tagged?
Testing & Maintenance - Do we know the gauges & over pressurisation devices work? If you interact with these barriers, others may depend on your actions.
Information, Competency & Training: Do we have the user manuals, experience and training to operate this equipment?
Control of work - how can this be improved? Purpose is to get the group to recognise importance of toolbox talks prior to work commencing and stopping
the job if people have concerns or don’t understand something.
Again, you may wish to flick back to Slide 5, run through them point by point to confirm.

## Slide 8: Under Pressure
Disclaimer: this safety moment is designed to prevent similar incidents occurring. All guidance herein is provided in good faith and Step Change in Safety nor its member companies accept responsibility for any inaccuracies or omissions contained within this safety moment.